## Slide 1: Buckling of Soft Cylinders
ES 242R Final Project
Helen Read

## Slide 2: Background
This is an ongoing project of my labmate, Yi Yang
  FEM work was previously done by David Melancon
We suction air out of thin-walled soft cylinders
Two regimes of behavior:
  (1) initial buckling event that creates folds and
  (2) twisting of cylinder (for # folds > 2)

## Slide 3: Background
The initial regime of buckling is well understood
  Can be captured by a buckling step in abaqus
  An analytical model exists too!
The post-buckling twisting behavior is less well understood

## Slide 4: Can we understand post-buckling behavior of soft cylinders?

## Slide 5: Simulation Setup
We have 3 parts
  2 caps (free and fixed)
  1 shell
For simplicity, we fix the edge of the cylindrical shell instead of modeling the fixed cap
All elements used are shells, currently S4R

## Slide 6: Simulation Setup
Current mesh size is
  Helps resolve the shape of the folds
  Makes the post-buckling simulation take a very long time
Simulation takes 2 separate steps
  (1) Linear buckling analysis  gives eigenmodes
  (2) Dynamic implicit w/ imperfections from the first eigenmode

## Slide 7: Current State

## Slide 8: Current State
time
2nd buckling event?
1st buckling event

## Slide 9: Overall plan
Investigate if the twist is a buckling event
  Run dynamic implicit up to “near” the initial twisting
  Run buckling analysis as a second step
  Do the two buckling modes Abaqus finds twist the same way?
In real life, where does this instability come from?
Can we create a simpler model for this system?
  Beam model using the # of beams to match # folds
p

## Slide 10: Questions/Comments/Suggestions?